## Slide 1: Arduino Workshop (ESP32 Advanced Level) ดร. วาธิส ลีลาภัทร ภาควิชาวิศวกรรมคอมพิวเตอร์ คณะวิศวกรรมศาสตร์ มหาวิทยาลัยขอนแก่น

## Slide 2: Agenda
Content
    ESP32 Wi-Fi Communications
    ESP32 Simple Web Server
    Internet of Things (IoT) using Blynk Platform
    Hardware interrupt
    LCD Custom font
Prerequisite:
1. Basic C/C++ programming language (Arduino IDE)
2. Basic and intermediate ESP32 courses
3. Electronics (not required, but will be advantageous)

## Slide 3: ESP32 DEVKIT
ESP-WROOM-32 DevKit
utilizes ESP32 chip, 240MHz, RAM 512KB, 4MB flash memory
Wi-Fi 2.4GHz / Bluetooth

## Slide 4: ESP32 DEVKIT Pinout
Micro USB Port

## Slide 5: ESP32 Extension Board
Pins extension
External power supply
S (Signal) Pins
V (3V Power supply) Pins
G (Ground) Pins

## Slide 6: Circuit Construction
Prototyping board
Pre-connected conductor stripes
Horizontal stripes on 2 top rows and 2 bottom rows
Vertical stripes in the middle

## Slide 7: Arduino Reference Sheet
https://kku.world/e664b0

## Slide 8
Hardware Interrupt
Interrupt is a mechanism in microcontroller to handle event triggered
by software or internal/external hardware
Interrupt can reduce processor load significantly when monitoring
signal from hardware
Read GPIO 2
Read GPIO 1
Read GPIO n
Routine for GPIO n
Routine for GPIO 2
Routine for GPIO 1
I/O Scan
Next statements
I/O Polling
Advantages:
Implemented in software only
Disadvantages:
Use more CPU time to execute
Slow response
Cannot be used during sleep mode
Main loop

## Slide 9
Hardware Interrupt
Interrupt is a mechanism in microcontroller to handle event triggered
by software or internal/external hardware
Interrupt can reduce processor load significantly when monitoring
signal from hardware
Interrupt
Interrupt Service Routine (ISR)
Go to
Routing for GPIO1 if signal is from GPIO1
Routine for GPIO2 if signal is from GPIO1
Routine for GPIO n if signal is from GPIO n
Statement 3
Statement 2
Statement 1
Statement n
Interrupt signal
This process is
handled by hardware
Advantages:
Fast response
Free CPU for another task
Can be used during sleep mode
Disadvantages:
Require hardware support
Main loop

## Slide 10
Hardware Interrupt
ESP32
D23
V
D19
GND
Push-button
Switch
10K Ohm
GND
Push-button
Switch
10K Ohm
V

## Slide 11
Hardware Interrupt
I/O polling example: BasicTwoButton.ino
Open serial monitor to see result
#define Up 17 //Increase value
#define Down 16 //Decrease value
int Counter = 0;
void setup() {
Serial.begin(9600);
pinMode(Up, OUTPUT);
pinMode(Down, OUTPUT);
}
void loop() {
Serial.println(Counter);
if(digitalRead(Up) == 1) Counter++; if(digitalRead(Down) == 1) Counter--;
delay(100);
}

## Slide 12
Hardware Interrupt
I/O polling example: InterruptTwoButton.ino
Open serial monitor to see result
#define Up 17 //Increase value
#define Down 16 //Decrease value
int Counter = 0;
void IRAM_ATTR Up_isr(){
Counter++;
}
void IRAM_ATTR Down_isr(){
Counter--;
}
void setup() {
Serial.begin(9600);
pinMode(Up, OUTPUT);
pinMode(Down, OUTPUT);
attachInterrupt(Up, Up_isr, RISING); attachInterrupt(Down, Down_isr, RISING);
}
void loop() {
  Serial.println(Counter);
delay(100);
}
Rising Edge
Falling Edge

## Slide 13
ESP32 Wi-Fi Operating Modes
ESP32 can operate in 2 different modes:
Station mode
Soft Access Point mode
2.4 GHz. band only

## Slide 14
ESP32 Wi-Fi Operating Modes
ESP32 can operate in three different modes:
Station mode
Soft Access Point mode
2.4 GHz. band only

## Slide 15
Example 1 : Wi-Fi Scanner
void setup() {
…
WiFi.mode(WIFI_STA); // Set WiFi to station mode
WiFi.disconnect(); // Disconnect from AP if it was previously connected
…
This example scans available Wi-Fi access points and displays
AP information.
Go to File  Examples  WiFi  WiFiScan

## Slide 16
Example 1 : Wi-Fi Scanner
// WiFi.scanNetworks will return the number of networks found
int n = WiFi.scanNetworks();
Serial.println("scan done");
if (n == 0) {
Serial.println("no networks found");
} else {
Serial.print(n);
Serial.println(" networks found");
for (int i = 0; i < n; ++i) {
// Print SSID and RSSI (Received Signal Strength Indicator) for each network found
Serial.print(i + 1);
Serial.print(": ");
Serial.print(WiFi.SSID(i)); //WiFi.SSID()  access point name
Serial.print(" (");
Serial.print(WiFi.RSSI(i)); //WiFi.RSSI()  access point signal

## Slide 17
Example 1 : Wi-Fi Scanner
1: Tenda_A32520 (-58)*
2: WXYZ_2.4GHz (-63)*
AP name
Signal Strength (dB)
Authentication required

## Slide 18
Example 2 : Hello Server
This example setups very simple web server on ESP32
Go to File  Examples  WebServer  HelloServer
const char* ssid = “……….."; //AP name
const char* password = “………."; //Password
const char* ssid = “Note7"; //AP name
const char* password = “qwerty1234"; //Password

## Slide 19
Example 2 : Hello Server
Connected to Tenda_A32520
IP address: 192.168.0.101
MDNS responder started
HTTP server started
IP Address of ESP32
Open your browser and type above IP address in address bar
hello from esp32!

## Slide 20
Example 2 : Hello Server
What is a Web server and how it works?
Web server stores, processes and delivers web pages to Web clients.
Web client is nothing but a web browser
The communication between client and server takes place using a protocol called Hypertext Transfer Protocol (HTTP).
Browser (user) ESP32

## Slide 21
HTTP Protocol

## Slide 22
HTTP Protocol
Client (browser) sends HTTP request to server
GET /index.html HTTP/1.1
Host: www.example.com
User-Agent: Mozilla/5.0
Accept: text/html, */*
Accept-Language: en-us
Accept-Charset: ISO-8859-1,utf-8
Connection: keep-alive
blank line
Header
Body
(optional)
method
URL
protocol version

## Slide 23
HTTP Protocol
HTTP Methods (Verbs)
● GET - Fetch a URL
● HEAD - Fetch information about a URL
● PUT - Store to an URL
● POST - Send form data to a URL and get a response back
● DELETE - Delete a URL
GET and POST (forms) are commonly used.
REST APIs used GET, PUT, POST, and DELETE

## Slide 24
Example 2 : Hello Server
HTTP Response from web server to client (browser)
HTTP/1.1 200 OK
Date: Thu, 24 Jul 2008 17:36:27 GMT
Server: Apache-Coyote/1.1
Content-Type: text/html;charset=UTF-8
Content-Length: 1846
blank line
<?xml ... >
<!DOCTYPE html ... >
<html ... >
...
</html>
Header
Body
(html)
protocol version
status status message

## Slide 25
HTTP Protocol
Common HTTP Response Status Codes
200 OK Success
307 Temporary Redirect Redirection - Browser retries using Location header
404 Not Found Famous one
503 Service Unavailable Something crashed on the server
500 Internal Server Error Something is messed up on the server
501 Not Implemented Coming
400 Bad Request Use if web app sends bogus request
401 Unauthorized Use if user isn't logged in
403 Forbidden Use if even logging in wouldn't help
550 Permission denied Not allow to perform request

## Slide 26
Example 3 : Advanced Web Server
This example setups more complicated web server on ESP32
Go to File  Examples  WebServer  AdvancedWebServer
const char* ssid = “……….."; //AP name
const char* password = “………."; //Password
const char* ssid = “Note7"; //AP name
const char* password = “qwerty1234"; //Password

## Slide 27
Example 3 : Advanced Web Server
Connected to Tenda_A32520
IP address: 192.168.0.101
MDNS responder started
HTTP server started
IP Address of ESP32
Open your browser and type above IP address in address bar

## Slide 28
Example 3 : Advanced Web Server
Concept
Connect to AP and get IP address
Setup web server
Create web content
    Text message & up timer
    Random numbers and graphic plot
    Timer
Create connection handling
Start web server & wait for connection

## Slide 29
Example 4 : Web Server Controlled LED
This example shows how to control LED from web browser
Go to File  Examples  WiFi  SimpleWiFiServer
const char* ssid = “……….."; //AP name
const char* password = “………."; //Password
const char* ssid = “Note7"; //AP name
const char* password = “qwerty1234"; //Password

## Slide 30
Example 4 : Simple Wi-Fi Server
Hardware setup
ESP32
D5
GND
1K Ohm

## Slide 31
Example 4 : Simple Wi-Fi Server
Connected to Tenda_A32520
IP address: 192.168.0.101
MDNS responder started
HTTP server started
IP Address of ESP32
Open your browser and type above IP address in address bar

## Slide 32
Example 4 : Simple Wi-Fi Server
Hardware setup

## Slide 33
Example 4 : Simple Wi-Fi Server
Concept
Connect to AP and get IP address
Setup web server
Create web content
Create connection handling
Start web server & wait for connection
If request is “GET /H” then Pin5  “1”
If request is “GET /L” then Pin5  “0”

## Slide 34
Example 5 : Switch Status Server
Hardware setup
This example shows how to use web server to display switch status
Open example file: InputSW-WebServer.ino
ESP32
V
D17
Push-button Switch
GND
D13
GND
1K Ohm
10K Ohm

## Slide 35
Connected to Tenda_A32520
IP address: 192.168.0.101
MDNS responder started
HTTP server started
IP Address of ESP32
Open your browser and type above IP address in address bar
Example 5 : Switch Status Server

## Slide 36
Concept
Connect to AP and get IP address
Setup web server
Create web content
Create connection handling
Start web server & wait for connection
Keep scanning the input pin and update web content
Example 5 : Switch Status Server

## Slide 37
Architecture of IoT
IoT platform

## Slide 38
Basic IoT application development
IoT applications require a lot of customized HW and SW
Common parts in IoT applications are user interface
There are available platform for creating simple IoT apps
    Blynk
    NetPie (by NECTEC)
    ThingWorx

## Slide 39
IoT Applications Development using Blynk
Blynk is an IoT Application development platform consisting of:
User interface for desktop and mobile devices (Android/iPhone)
Connection library for various IoT hardware platforms

## Slide 40
Blynk Applications Development
Signup for Blynk by going to: http://blynk.io
Type your email address to proceed to the next step

## Slide 41
Open your email, then set a new password
Go back to main screen, log in using your new password
Once you log in, you will see Blynk Console
Steps to create a Blynk application are as follows:
  Create new template in Blynk console
  Create device for your template
  Create user interface in Blynk mobile app
  Build your circuit and write code for ESP32
Blynk Applications Development

## Slide 42
Creating a new template in Blynk Console
Click on Developer Zone on the left menu to go to template
Then click on New template

## Slide 43
Under Name, type “LED Control” then select EPS32 and WiFi
Click on Done button
Creating a new template in Blynk Console
ESP32

## Slide 44
The next step is to create new datastream by clicking on
Datastreams tab and then New datastream button
Creating a new template in Blynk Console

## Slide 45
After new datastream is created, choose Virtual Pin
Creating a new template in Blynk Console

## Slide 46
At the bottom of Virtual Pin Datastream setup screen, click on Create button
Creating a new template in Blynk Console

## Slide 47
Repeat creating Virtual Pin Datastream again by clicking at New datastream
Creating a new template in Blynk Console

## Slide 48
Now Datastreams tab should look like this:
Creating a new template in Blynk Console

## Slide 49
Go to Web Dashboard then drag Switch from widget box and place on the Dashboard
Creating a new template in Blynk Console

## Slide 50
Move mouse pointer over Switch widget, then click on setting icon
Creating a new template in Blynk Console

## Slide 51
Under Title, type LED1, then set Datastream to Integer V0 [V0]
then click on Save
Creating a new template in Blynk Console

## Slide 52
Repeat this process for setting the other Switch
Click on Save when finish
Creating a new template in Blynk Console

## Slide 53
Finally, click on Save button on the right
Creating a new template in Blynk Console

## Slide 54
Creating device in Blynk Console
Next, choose Devices from menu on the left
Then, click on + New Device

## Slide 55
Choose From template
Creating device in Blynk Console

## Slide 56
Choose the template we have created
Choose LED Control, then click on Create
Creating device in Blynk Console

## Slide 57
New Device Created! message will be displayed
We need to copy the Template ID, Name and AuthToken into our sketch
Creating device in Blynk Console

## Slide 58
Test circuit for Blynk Application
ESP32
GND
GPIO23
GPIO19
680 Ohm
680 Ohm

## Slide 59
Install Blynk Library in Arduino IDE
Go to menu Tools  Manage Libraries…
Type Blynk in search box
Click install on Blynk library
Version 1.3.2

## Slide 60
Blynk sketch for ESP32
Download Blynk_LED_ESP32.ino sketch from
https://github.com/watisleelapatra/Arduino
Open the sketch in Arduino IDE
Paste the following lines in the sketch
Information from
Blynk Console
Example
#define BLYNK_TEMPLATE_ID " "
#define BLYNK_TEMPLATE_NAME " "
#define BLYNK_AUTH_TOKEN " "

## Slide 61
Add your WiFi AP and password in the sketch
Wi-Fi AP name
Password for Wi-Fi AP
char ssid[] = " ";
char pass[] = " ";
Then download the sketch
Blynk sketch for ESP32

## Slide 62
Install Blynk IoT Mobile Application
Go to App Store (iPhone) or Google Play (Android)
Search and install Blynk IoT on your mobile phone
After installation, Login using email you for signing up
There will be the created Template, Choose LED Control
1
2
3
4

## Slide 63
Creating Mobile Application
After choosing LED Control template, click on the wrench icon
Add widget by tapping  icon
Then choose Button

## Slide 64
A button will be shown, then tap on the button
Change MODE from Push to Switch
Then set DATASTREAM to Integer V0 [V0]
Creating Mobile Application

## Slide 65
Repeat the process, tap on  then choose Button
Change Mode to Switch and set DATASTREAM to Integer V1 [V1]
Tap  icon (top left of the screen) to go back to Application main screen
Creating Mobile Application

## Slide 66
Create a new template in Blynk Console, go to Developer zone and click on
New template
Type DHT11 under Name, choose ESP32 for Hardware and WiFi for Connection Type
Sending DHT11 data to Blynk IoT App
ESP32

## Slide 67
Add Virtual Pin for DATASTREAM and set other parameters as follow:
Sending DHT11 data to Blynk IoT App

## Slide 68
Add 2nd DATASTREAM by choosing Virtual Pin and set parameters as follow:
Sending DHT11 data to Blynk IoT App

## Slide 69
Finally, click on Save And Apply
Sending DHT11 data to Blynk IoT App

## Slide 70
Next, go to Devices menu and click on +New Device
Click on From template
Sending DHT11 data to Blynk IoT App

## Slide 71
Choose DHT11 for Template , then click Create
Sending DHT11 data to Blynk IoT App

## Slide 72
Template ID, Template Name and Token will be generated
Click on Copy to clipboard, then paste these information in your sketch
Sending DHT11 data to Blynk IoT App

## Slide 73
Build the following circuit on breadboard
Download Blynk_DHT11_ESP32.ino sketch from https://github.com/watisleelapatra/Arduino
Sending DHT11 data to Blynk IoT App
ESP32
GND
3V
D13

## Slide 74
Add Template ID, Name and AuthToken from Blynk console in your sketch
Add Wi-Fi AP name and Password, then download sketch to ESP32
Sending DHT11 data to Blynk IoT App

## Slide 75
Open Blynk IoT App on mobile phone
Choose DHT11 Display template
Add Gauge Widget and rename to Temperature and set DATASTREAM to Integer V0 [V0]
Sending DHT11 data to Blynk IoT App

## Slide 76
Add the 2nd Gauge, rename it to Humidity, set DATASTREAM to Integer V1 [V1]
Tap on X to close current screen, then tap on  to go back to main screen
Sending DHT11 data to Blynk IoT App

## Slide 77
Data from DHT11 will be displayed and updated every 5 seconds
Sending DHT11 data to Blynk IoT App

## Slide 78
Alphanumeric LCD (revisited)
Inter-Integrated Circuit (IIC or I2C) is used to simplified communication
between LCD module and ESP32
I2C uses only 2 I/O lines for communication
I2C controller board
ESP32
GND
5V
D22
D21
LCD
SDA
SCL
GND
Vcc
Contrast adjust

## Slide 79
Alphanumeric LCD
Floating point numbers can be printed with specified number of fraction
Run test code: I2C_LCD_Numbers.ino
LCD display contain preloaded special characters:
  To print these characters,
  use (char) x inside lcd.print()
  For example:
  lcd.print((char) 247); // print 

## Slide 80
Some applications, we might need special symbols that
are not available in LCD character ROM
It is possible to customize fonts and display them on LCD
LCD Custom Font Display

## Slide 81
Each character in LCD fonts are contained in 5x8 pixel grid
We consider dark pixel as "1" and light pixel as "0"
In the example below, we can write binary number for each row as:
LCD Custom Font Display
00001
11001
11001
01001
01001
01001
01001
01111
#include <Wire.h>
#include <LiquidCrystal_I2C.h>
LiquidCrystal_I2C lcd(0x3F, 16, 2);
byte customChar[] = {
B00001, B11001, B11001, B01001,
B01001, B01001, B01001, B01111
};
void setup() { // Initialize the LCD
lcd.init();
for (int i = 0; i < 8; i++) { // Create custom characters
lcd.createChar(i, thaiChars[i]);
}
lcd.clear();
displayThaiCharacters(); // Display the Thai characters
}

## Slide 82
There is an online tool to help design custom fonts:
https://maxpromer.github.io/LCD-Character-Creator/
LCD Custom Font Display

## Slide 83
The Liquid_Crystal_I2C library provides function to install
custom fonts into available LCD character memory
Example: ThaiCharDemo.ino
LCD Custom Font Display